## Slide 1: System Design and Hydraulics
Slide 4 - 1
S-211
Portable Pumps and Water Use
Unit 4 – System Design and Hydraulics
Unit 4

## Slide 2: Words of Experience
Click icon to hear firefighter story about pumps.

## Slide 3: Objectives
List one reason it is important for a pump and nozzle operator to have a basic understanding of hydraulics.
Given scenarios, determine flow and pump discharge pressure, and select appropriate pump(s).

## Slide 4: Objectives
Given scenarios, draw a schematic of the design of a water delivery system, and troubleshoot the delivery system.
Given scenarios, determine whether parallel hose lay, series pumping, or parallel pumping would be the best option.

## Slide 5
Introduction

## Slide 7
How does the crew boss, squad boss, or pump operator determine….
  What pumping configuration(s) will work?
  What hose lay design will work?
  What type of nozzle(s) to use?

## Slide 8: Making Decisions
Trial and error (not always the best way)
Planning ahead (reduces guesswork)

## Slide 9: Hydraulics is the science and engineering that deals with fluids at rest and in motion.

## Slide 10: Why is hydraulics important?
To ensure proper amount of water and pressure is delivered to the nozzle(s).
To determine equipment needed, keep it working, and prevent damage.
To design and troubleshoot the water delivery system.
To help ensure a safe work environment.

## Slide 11
Three-step process

## Slide 12
Step 1 – Determine flow rate (gpm).
Step 2 – Calculate Pump Discharge Pressure (psi).
Step 3 – Determine what types of pumps are capable of providing flow and PDP.

## Slide 13: hose lays with no laterals

## Slide 14: Three-Step Process
Step 1 – Determine flow rate.
Step 2 – Calculate Pump Discharge Pressure (PDP).
Step 3 – Determine what types of pumps are capable of providing flow and PDP.

## Slide 15: Step 1 – Determine Flow Rate
The type of nozzle(s) on the hose lay determines flow rate, for example:
Twin Tip
Adjustable Barrel

## Slide 16
Refer to IRPG for flow rates of commonly used nozzles.
Step 1 – Determine Flow Rate

## Slide 17: Step 1 – Determine Flow Rate
Click on the calculator image above to launch the Interactive Calculator application.
If for some reason the link is broken, locate the file named “Calculator_gui.exe,” and double click on it to start.

## Slide 18: Practice
What is the flow rate from a 3/8" tip at 50 psi?
  Answer: 30 gpm

## Slide 19: Three Step Process
Step 1 – Determine flow rate.
Step 2 – Calculate Pump Discharge Pressure (PDP).
Step 3 – Determine what types of pumps are capable of providing flow and PDP.

## Slide 20
NP ± HP + FL = PDP
NP = Nozzle Pressure
HP = Head Pressure
FL = Friction Loss
PDP = Pump Discharge Pressure

## Slide 21: NP ± HP + FL = PDP
Nozzle Pressure (NP) = Pressure (psi) the nozzle is designed to operate at most efficiently.
Click on the image to play animation.
NP

## Slide 22
Twin tip nozzle – 50 psi
Adjustable barrel nozzle – 100 psi
NP ± HP + FL = PDP

## Slide 23: NP ± HP + FL = PDP
Refer to IRPG for nozzle pressures.

## Slide 24: NP ± HP + FL = PDP
Head Pressure (HP) = Pressure (psi) exerted by a column of water.
Click on the image to play animation.

## Slide 25: NP ± HP + FL = PDP
±HP | = | Number of feet in elevation change from pump to nozzle | ÷ | 2 psi/1'
Uphill: Add HP.
Downhill: Subtract HP.
Level ground: HP = 0.

## Slide 26: NP ± HP + FL = PDP
General Rule: HP is 1/2 the elevation rise or fall.

## Slide 27: Practice
  The nozzle is 250' (elevation change) uphill from the pump. What is the head pressure?
      Answer: +125 psi
  The nozzle is 100' (elevation change) downhill from the pump. What is the head pressure?
      Answer: -50 psi
  The nozzle is 250' (elevation change) downhill from the pump. What is the head pressure?
      Answer: -125 psi

## Slide 28: NP ± HP + FL = PDP
Click on the image to play animation.
Friction Loss (FL) = Loss of pressure due to water turbulence and resistance along the inside wall of the hose.

## Slide 29: NP ± HP + FL = PDP
Why is friction loss important?
  The pump has to overcome the loss of pressure (from friction in the hose lay) to provide adequate pressure to the nozzle.

## Slide 30: NP ± HP + FL = PDP
FL per 100' section of hose lay | x | Number of 100' sections of hose lay | = | Total FL for hose lay
To determine FL per 100' section of hose lay you will need to know flow and hose diameter; and then refer to the the IRPG or friction loss calculator.

## Slide 31: NP ± HP + FL = PDP
What is the total friction loss for 100' of 1" hose with flow rate of 30 gpm?
Answer: 23 psi
FL per 100' section of hose lay | x | Number of 100' sections of hose lay | = | Total FL for hose lay

## Slide 32: Practice
FL per 100' section of hose lay | x | Number of 100' sections of hose lay | = | Total FL for hose lay
 | x |  | = | 
100' of 1½"
100' of 1½"
100' of 1½"
Flow = 30 gpm
What is total FL for 300' of 1½" hose @ 30 gpm?
3 psi
3psi
3 psi
3 psi
3
9 psi

## Slide 33: NP ± HP + FL = PDP
Click on the calculator image above to launch the Interactive Calculator application.
If for some reason the link is broken, just locate the file named “Calculator_gui.exe,” double click on it to start.
FL per 100' section of hose lay | x | Number of 100' sections of hose lay | = | Total FL for hose lay

## Slide 34: Practice
FL per 100' section of hose lay | x | Number of 100' sections of hose lay | = | Total FL for hose lay
 | x |  | = | 
100' of 1"
100' of 1"
100' of 1"
Flow = 30 gpm
What is total FL for 300' of 1" hose @ 30 gpm?
23 psi
23psi
23 psi
23 psi
3
69 psi

## Slide 35: Practice
What is total FL for 300' of ¾" hose @ 30 gpm?
FL per 100' section of hose lay | x | Number of 100' sections of hose lay | = | Total friction loss
100 psi | x | 3 | = | 300 psi
100' of ¾"
100' of ¾"
100' of ¾"
Flow = 30 gpm
100 psi
100 psi
100 psi

## Slide 36: Friction Loss Principles
Friction loss principles help explain the RELATIONSHIP between friction loss and flow, hose diameter, and hose length.

## Slide 37: Friction Loss Principle:
When FLOW (gpm) decreases, friction loss decreases (when hose diameter is constant).
Click on the image to play animation.

## Slide 38: Practice
Flow rate is 40 gpm. What is friction loss in 1" hose?
  Answer: 40 psi per 100'
Flow rate is 20 gpm. What is friction loss in 1" hose?
  Answer: 10 psi per 100'
Link to Calculator

## Slide 39: Friction Loss Principle:
When HOSE DIAMETER INCREASES, friction loss DECREASES.
Click on the image to play animation.

## Slide 40: Practice
Flow rate is 30 gpm. What is the friction loss in 1" hose?
  Answer: 23 psi per 100'
Flow rate is 30 gpm. What is the friction loss in 1½" hose?
  Answer: 3 psi per 100'

## Slide 41: Friction Loss Principle:
Longer hose lengths have increased friction loss.
1½" ; 800'; flow = 30 gpm; friction loss = 24 psi
1½" ; 300'; flow = 30 gpm; friction loss = 9 psi

## Slide 42: Practice
Flow rate is 20 gpm. What is FL in 100' of 1" hose?
100' of 1"
Flow = 20 gpm
FL = 10 psi
  Answer: 10 psi

## Slide 43: Practice
Flow rate is 20 gpm.
What is friction loss in 300' of 1" hose?
100'of 1"
100' of 1"
100' of 1"
FL = 10 psi
FL = 10 psi
FL = 10 psi
Flow = 20 gpm
Answer: 30 psi

## Slide 44: NP ± HP + FL = PDP
Step 1 – Determine flow rate (gpm).
Step 2 – Calculate Pump Discharge Pressure (psi).
Step 3 – Determine what types of pumps are capable of providing flow and PDP.
PDP = the pressure (psi) required to deliver a specific pressure and flow at the nozzle.

## Slide 45: Scenario A
  The hose lay has 500' of 1½" hose; one Forester nozzle with a 3/8" tip attached. There is no elevation difference between the nozzle and pump.
  Step 1: What is flow rate?
  Step 2: What is PDP?
500' of 1½"
3/8" Tip

## Slide 46: Scenario A
Link to Calculator
Step 1: Flow rate | = | 30 gpm
Step 2: PDP | = | 65 psi
500' of 1½"
3/8 " Tip
FL = 3 psi
FL = 3 psi
FL = 3 psi
FL = 3 psi
FL = 3 psi
NP | = | +50 psi
±HP | = | 0 psi
FL | = | +15 psi
PDP | = | 65 psi
Flow = 30 gpm

## Slide 47: Three Step Process
Step 1: What is flow rate?
Step 2: What is PDP?
Step 3: Identify types of pumps capable of providing flow and PDP.

## Slide 48: Scenario A
500' of 1½"
3/8" tip
FL = 3 psi
FL = 3 psi
FL = 3 psi
FL = 3 psi
FL = 3 psi
Step 1: Flow rate | = | 30 gpm
Step 2: PDP | = | 65 psi
Step 3: Identify Pump(s) |  | Mark 3; Wick 375
Refer to Pump Performance Chart
Flow = 30 gpm
Link to Calculator

## Slide 49: Scenario B
The hose lay has 1000' of 1½" hose; one Forester nozzle with 3/8" tip attached. Nozzle is located 50' above the pump.
  Step 1: What is flow rate?
  Step 2: What is PDP?
  Step 3: Identify types of pumps capable of providing flow and PDP.
1000' of 1½"
3/8" tip
50'

## Slide 50: Scenario B
Link to Calculator
Step 1: Flow rate | = | 30 gpm
Step 2: PDP | = | 105 psi
Step 3: Identify pump(s) |  | Mark 3; Wick 375
1000' of 1½"
3/8 " tip
50'
FL = 3 psi
FL = 3 psi
FL = 3 psi
FL = 3 psi
FL = 3 psi
FL = 3 psi
FL = 3 psi
FL = 3 psi
NP | = | +50 psi
+/-HP | = | +25 psi
FL | = | +30 psi
PDP | = | 105 psi
Flow = 30 gpm
FL = 3 psi
FL = 3 psi
Refer to Pump Performance Chart

## Slide 51: Scenario C
  The hose lay has 900' of 1" hose; one Forester nozzle with ¼" tip attached. Nozzle is located 150' above the pump.
  Step 1: What is flow rate?
  Step 2: What is PDP?
  Step 3: Identify types of pump capable of providing flow and PDP.
900' of 1"
¼" tip
150'

## Slide 52: Scenario C
900' of 1"
1/4" tip
150'
Step 1: Flow rate | = | 13 gpm
Step 2: PDP | = | 161 psi
Step 3: Identify pump(s) |  | 
NP | = | +50 psi
±HP | = | +75 psi
FL | = | +36 psi
PDP | = | 161 psi
FL = 4 psi
FL = 4 psi
FL = 4 psi
FL = 4 psi
FL = 4 psi
FL = 4 psi
FL = 4 psi
FL = 4 psi
FL = 4 psi
Link to Calculator
Flow = 13 gpm
Refer to Pump Performance Chart

## Slide 53: Scenario D
The hose lay has 1200' of 1½" hose; one 60 gpm adjustable barrel nozzle. Nozzle is located 180' below the pump.
  Step 1: What is flow rate?
  Step 2: What is PDP?
  Step 3: Identify pumps capable of providing flow and PDP.
180'
1200' of 1½"
Adjustable barrel nozzle

## Slide 54: Scenario D
Link to Calculator
1200' of 1½"
Adjustable barrel nozzle
Step 1: Flow rate | = | 60 gpm
Step 2: PDP | = | 166 psi
Step 3: Identify pump(s) |  | 
180'
NP | = | +100 psi
±HP | = | -90 psi
FL | = | +156 psi
PDP | = | 166 psi
FL = 13 psi
FL = 13 psi
FL = 13 psi
FL = 13 psi
FL = 13 psi
FL = 13 psi
FL = 13 psi
FL = 13 psi
Link to Calculator
Flow = 60 gpm
Refer to Pump Performance Chart
FL = 13 psi
FL = 13 psi
FL = 13 psi
FL = 13 psi

## Slide 55: hose lay (no laterals) with different size hoses

## Slide 56: When a hose lay has different size hoses, how does the step-by-step process change?
Step 1: Flow rate (same process)
Step 2: PDP
  NP (same process)
  HP (same process)
  Friction loss (different process)
    Friction loss is calculated for each hose size and then added together to get total friction loss.
Step 3: Identify pump (same process)

## Slide 57: Scenario E
The hose lay has 500' of 1½" hose, which is reduced down to 100' of 1" hose. One Forester nozzle with 3/8" tip attached. There is no elevation difference between the pump and the nozzle.
  Step 1: What is flow rate?
  Step 2: What is PDP?
  Step 3: Identify pumps capable of providing flow and PDP.
500' of 1½"
3/8" tip
100' of 1"

## Slide 58: Scenario E
Step 1: Flow rate | = | 30 gpm
Step 2: PDP | = | 88 psi
Step 3: Identify pump(s) |  | 
Link to Calculator
500' of 1½"
3/8" tip
100' of 1"
NP | = | +50 psi
±HP | = | 0 psi
FL | = | +38 psi
PDP | = | 88 psi
FL = 23 psi
FL = 15 psi
Link to Calculator
Flow = 30 gpm
Refer to Pump Performance Chart

## Slide 59: hose lay with laterals

## Slide 60: When a hose lay has laterals, how does the step-by-step process change?
Step 1: Flow rate (slightly different process)
  Calculate flow in all laterals to determine flow rate in each section of the trunk.
Step 2: PDP
  Nozzle pressure (same process)
  Head pressure (same process)
  Friction loss (slightly different process)
    Calculate FL for only 1 lateral.
    Calculate FL for each section of the trunk.
Step 3: Identify pumps (same process)

## Slide 61: Scenario F
The hose lay has 300' of 1½" hose with a gated wye that goes into two 100' 1" laterals, each with ¼" tip. There is no elevation difference between the pump and nozzle.
  Step 1: What is flow rate?
  Step 2: What is PDP?
  Step 3: Identify pumps capable of providing flow and PDP.
1/4" tip
100' of 1"
300' of 1½"
1/4" tip
100' of 1"

## Slide 62: Scenario F
1/4" tip
100’ of 1"
300' of 1½"
1/4" tip
100’ of 1”
Trunk flow – 26 gpm
Lateral A flow – 13 gpm
Lateral B flow– 13 gpm
Lateral A FL = 4 psi
Trunk FL = 6 psi
Step 1: Flow rate Lateral A Lateral B Trunk | = = = | 13 gpm 13 gpm 26 gpm
Step 2: PDP Calculate FL for only 1 lateral and for each section of the trunk. | = | 60 psi
Step 3: Identify Pump(s) |  | 
NP | = | +50 psi
±HP | = | 0 psi
FL lateral A | = | +4 psi
FL trunk | = | +6 psi
PDP | = | 60 psi
Link to Calculator
Refer to Pump Performance Chart
Calculate flow in all laterals to determine flow rate in each section of the trunk.

## Slide 63: Scenario G
  The hose lay has 700' of 1½" hose until the first lateral. Then there is another 100' of 1½" hose to the second lateral and another 100' of 1½" hose to the third lateral. All laterals have 100' of 1" hose and ¼" tips. There is no elevation difference between the pump and nozzle.
  Step 1: What is flow rate?
  Step 2: What is PDP?
  Step 3: Identify pumps capable of providing flow and PDP.
100‘ of 1"
700' of 1½"
100' of 1"
100' of 1"
100'of 1½"
100' of 1½"
1/4" tip
1/4“ tip
1/4" tip

## Slide 64: Scenario G
100' of 1"
100' of 1"
100' of 1"
100' of 1½"
100' of 1½"
700' of 1½"
Step 1: Flow rate Lateral A Lateral B Lateral C Trunk Z Trunk Y Trunk X | = = = = = = | 13 gpm 13 gpm 13 gpm 13 gpm 26 gpm 39 gpm
Step 2: PDP | = | 91 psi
Step 3: Identify pump(s) |  | 
NP | = | 50 psi
±HP | = | 0 psi
FL lateral C | = | 4 psi
FL trunk Z | = | 0 psi
FL trunk Y | = | 2 psi
FL trunk X | = | 35 psi
PDP | = | 91 psi
Trunk X
Lateral A
Lateral B
Lateral C
Trunk Z
Trunk Y
1/4" tip
1/4" tip
1/4" tip
Calculate flow in all laterals to determine flow rate in each section of the trunk. These flow rates will also be used to determine friction loss.
Link to Calculator
Refer to Pump Performance Chart

## Slide 65: advanced water delivery Systems

## Slide 66: Scenario H
1200' of 1½"
60 gpm adjustable barrel nozzle
60'
Step 1: Flow rate | = | 60 gpm
Step 2: PDP | = | 286 psi
Step 3: Identify pumps |  | No pumps
NP | = | 100 psi
±HP | = | +30 psi
FL | = | 156 psi
PDP | = | 286 psi

## Slide 67: Parallel Hose Lay
What is the main advantage of a parallel hose lay?
What is a general guideline to determine the friction loss for a parallel hose lay?

## Slide 68: Will parallel hose lay work?
60'
 |  | Scenario H | Scenario H and Parallel Hose Lay Design
Step 1: Flow rate | = | 60 gpm | 60 gpm
Step 2: PDP | = | NP = +100 psi HP = +30 psi FL = +156 psi PDP = 286 psi | NP = +100 psi HP = +30 psi FL = +39 psi PDP = 169 psi
Step 3: Identify pump |  | No pumps | Mark 3; Wick 375.
Refer to Pump Performance Chart
The parallel hose lay reduces friction loss.

## Slide 69: Series Pumping
Increases pressure but not flow.
When using series pumping, pump pressures are combined, but flow stays the same.
For Example:
1 Mark 3 pump will produce 60 gpm at 170 psi. If another Mark 3 pump is added in series, the combination will produce 60 gpm at 340 psi.

## Slide 70: Will series pumping work?
60 gpm
60'
1200' of 1½"
 |  | Scenario H | Series Pumping and Scenario H
Step 1: Flow rate | = | 60 gpm | 60 gpm
Step 2: PDP | = | NP = +100 psi HP = +30 psi FL = +156 psi PDP = 286 psi | NP = +100 psi HP = +30 psi FL = +156 psi PDP = 286 psi
Step 3: Identify pump |  | No pumps alone can provide flow and PDP. | Use two pumps in series (Mark 3; Wick 375).
Refer to Pump Performance Chart
The Mark 3 can produce 60 gpm at 170 psi. If two Mark 3 pumps are set up as series pumping, they can provide 60 gpm at 340 psi. Since this hose lay requires 60 gpm at 286 psi – series pumping works.

## Slide 71: Parallel Pumping
General rule - doubles the flow but doesn’t increase pressure.
When pumps are used in parallel, flow from each pump is added together with no change in pressure.

## Slide 72: Will parallel pumping work?
60’
Slide 4 - 72
60 gpm
60'
1200' of 1½"
With parallel pumping, flow from each pump is added together with no change in pressure. The Mark 3 can produce 30 gpm at 285 psi. If two Mark 3 pumps are set up for parallel pumping then together they can provide 60 gpm at 286 psi. This is also true for the Wick 375 pump.
 |  | Scenario H | Parallel Pumping
Step 1: Flow rate | = | 60 gpm | 60 gpm
Step 2: PDP | = | NP = +100 psi HP = +30 psi FL = +156 psi PDP = 286 psi | NP = +100 psi HP = +30 psi FL = +156 psi PDP = 286 psi
Step 3: Identify pump |  | No pumps alone can provide flow and PDP. | Use two pumps in parallel (Mark 3; Wick 375).
Refer to Pump Performance Chart

## Slide 73: Review
Parallel Hose Lay |  | Reduces friction loss in hose lay.
Series Pumping |  | Increases pump performance – by using two pumps to increase pressure.
Parallel Pumping |  | Increases pump performance – by using two pumps to increase flow.

## Slide 74
Troubleshooting
the delivery system
from a Hydraulic perspective

## Slide 75: Troubleshooting – Factors to Consider
Pump discharge pressure
  Nozzle pressure – Change nozzle type, tip size, or both.
  Head pressure – Move pump to reduce elevation change.
  Friction loss – Reduce friction loss by increasing hose diameter, shortening hose length, using parallel hose lay, and/or reducing flow.
Pump capability
  Use a pump with higher performance capability.
  Use series pumping system to increase pressure.
  Use parallel pumping system to increase flow.

## Slide 76: Exercise
Troubleshooting a
Water Delivery System
From a
Hydraulic Perspective

## Slide 77: Exercise
Nozzle Pressure | = | +50 psi
Head Pressure | = | +200 psi
Friction Loss | = | +150 psi
PDP |  | 400 psi
FLOW | = | 60 gpm

## Slide 78
Designing a Water
delivery system using hydraulic concepts

## Slide 79: Delivery System Design

## Slide 80: Exercise
How to Design a Hydraulically Sound Water Delivery System

## Slide 81: Exercise
Your squad is mopping up a ½-acre spot fire burning in heavy slash. There is a 200' elevation change from the pump site (river) to the fire, and the distance is 2000'. The following equipment is available:
2 Mark 3 pumps
2 MK 26 pumps
2500' of 1½" hose
500' of 1" hose
3 Forester nozzles with 3/16" tip
3 adjustable barrel nozzles (1")
Assorted appliances and adapters

## Slide 82: Review

## Slide 83
1. Why is it important to understand hydraulic principles?
Possible answers:
  Ensure proper amount of water is delivered to the nozzle.
  Determine appropriate equipment for the job.
  Troubleshoot problems with the water delivery system.
  Reduce damage to equipment.

## Slide 84
2. The hose lay has 500' of 1½" hose, and one Forester nozzle with a 3/8" tip is attached. The nozzle is 30' above the pump.
a) What is flow?
b) What is PDP?
c) Identify pumps capable of providing flow and PDP.
  Answer:
  a) Flow = 30 gpm
  b) PDP = 80 psi
    NP = +50 psi
    HP = +15 psi
    FL = +15 psi
    PDP = 80 psi
  c) Mark-3 and Wick 375
Link to Calculator

## Slide 85
3. What is the definition of pump discharge pressure (PDP)? Where is pump discharge pressure measured?
  Answer: PDP is the pressure required to deliver a specific pressure and flow at the nozzle.
  PDP is measured at the pump panel.

## Slide 86
4. When the nozzle is located uphill from the pump, do you subtract or add head pressure in the PDP formula?
Answer: Add

## Slide 87
5. When hose diameter increases, does friction loss increase or decrease?
  Answer: Decrease

## Slide 88
6. When flow (gpm) decreases, does friction loss increase or decrease?
  Answer: Decrease

## Slide 89
7. Do longer hose lengths have more or less friction loss than shorter hose lengths (of same diameter)?
  Answer: More

## Slide 90
  8. If there is significant elevation rise from the pump to the nozzle and one pump cannot provide the pressure that is needed, which multiple pump system would most likely solve the problem – series pumping or parallel pumping?
    Answer: Series pumping

## Slide 91
  9. You are filling a drop tank, and it is going slow. You want to increase the flow to speed it up. What pump configuration would you use – series pumping or parallel pumping?
    Answer: Parallel pumping

## Slide 92
  10. What impact do parallel lines have on friction loss – increase friction loss or decrease friction loss?
  Answer: Decrease

## Slide 93
11. Friction loss needs to be reduced. What options should be considered?
  Possible Answers:
    Increase hose diameter.
    Shorten hose length.
    Use a parallel hose lay.
    Reduce flow.

## Slide 94: Objectives
List one reason it is important for a pump and nozzle operator to have a basic understanding of hydraulics.
Given scenarios, determine flow and pump discharge pressure, and select appropriate pump(s).

## Slide 95: Objectives
Given scenarios, draw a schematic of the design of a water delivery system, and troubleshoot the delivery system.
Given scenarios, determine whether parallel hose lay, series pumping, or parallel pumping would be the best option.