## Slide 1: Aircraft missions
Unit 3

## Slide 2: Unit 3 Objectives
1. Define tactical and logistical use of aircraft.
Identify the advantages and disadvantages of the various tactical aircraft missions.
Identify the different logistical aircraft missions and their purpose.

## Slide 3: Unit 3 Objectives
4. Describe the proper air-to-ground communication procedures.
Describe safety procedures to follow during aerial fire suppression operations.
Describe Special Operations.

## Slide 4: Tactical Aircraft Missions

## Slide 5: Tactical Aircraft Missions
Tactical aircraft missions can be defined as any mission that uses an aircraft to accomplish a specific tactical task during fire suppression efforts, e.g., aerial fire suppressant delivery, deliver smokejumpers, transport firefighters and equipment, rappeller delivery, and aerial ignition.

## Slide 6: Aerial Fire Suppressants Delivery
Both airplanes and helicopters are used to drop aerial fire suppressants (retardant, water, gel, and foam) onto a wildland fire in an effort to slow its advancement and to contain the fire.
Very effective during initial attack.

## Slide 7: air tanker/seat Advantages
Large volumes
Multiple drop capability
Fast travel times
Good for initial attack

## Slide 8: air tanker/seat disadvantages
Nonaccessible terrain
Long turnaround times
Less accurate than helicopters
Single purpose use
Interrupt other aircraft missions
Only about 20 to 24 Federal large air tankers available in any given year

## Slide 9: Helicopter Advantages
Drop more gallons per hour if a close source is available.
Used for other types of missions.
Work in steep terrain.
Make accurate drops near homes.

## Slide 10: Helicopter disadvantages
Helicopters have wind limitations affecting their use in high winds.
Limited by size, payload, airspeed, and range.
Weather and daylight dependent.

## Slide 11: Smokejumper Advantages
Rapid delivery of firefighters
No aircraft landing area required
Self-supporting for two shifts
Aircraft can deliver fire supplies and equipment (paracargo)

## Slide 12: Smokejumper Disadvantages
High training & equipment costs
Can’t jump in high winds
Logistics of retrieval (pack out)
Weather and daylight dependent

## Slide 13
Fire Crews and Equipment Delivery
Aircraft have the ability to rapidly
deliver for tactical assignment:
Firefighters, crews, and their equipment

## Slide 14: Helitack
Aerially delivered firefighters specially
trained in helicopters operations are
called helitack crews.
Effective for initial attack.

## Slide 15: Helitack advantages
Rapid aerial delivery of firefighters to remote areas
Self-supporting for two shifts

## Slide 16: helitack Disadvantages
Dependent on natural or preestablished landing areas
Limited by aircraft size, airspeed, and range
Weather and daylight dependent

## Slide 17: rappelling
Rappelling is delivering firefighters to an area where it is impossible or unsafe to land a helicopter.
Firefighters descend down ropes from a hovering helicopter.
Can be effective for initial attack in remote areas.

## Slide 18: Rappelling advantages
Rapid delivery of firefighters to remote areas.
No landing area is required.
Self-supporting for two shifts.
Rappel helicopter can be used to deliver firefighting supplies and equipment and for water bucket work.

## Slide 19: rappelling Disadvantages
Higher training and equipment cost.
Limited by aircraft size, airspeed, and range.
Limited to rappel rope length.
Unable to hover in high winds to let down rappellers.
Weather and daylight dependent.

## Slide 20: Aerial ignition
Aerial ignition systems are used to apply fire on the ground from the air to assist in the containment and control during fire suppression efforts.

## Slide 21: Aerial ignition
Ignition is done quicker than ground igniting methods.
Ignition can cover a large area.
Area to be burned is inaccessible or unsafe for people on the ground to accomplish.

## Slide 22: Logistical Missions
Any aviation activities that support suppression of a fire or project but are not in themselves tactical.

## Slide 23: Transportation of People and Supplies
People or equipment must be moved long distances.
When ground transport methods are not feasible.
Short timeframe exists to meet the needs of the fire suppression efforts.
Aircraft may range from a light single-engine to a large Boeing 737.

## Slide 24: Single-Engine

## Slide 25
Large Transport Aircraft

## Slide 26: Paracargo Drop

## Slide 27
Paracargo drop zone
safety requirements

## Slide 28: Helicopters
transport equipment and supplies internally and externally.

## Slide 29: External Cargo rack

## Slide 30: Sling Loads
require qualified personnel.

## Slide 31: Fire Perimeter Mapping
A Field Observer (FOBS) from the Planning Section will be onboard the aircraft with a global positioning system (GPS).
As the aircraft flies the perimeter, the FOBS will enter waypoints of the perimeter into the GPS unit.

## Slide 32: Detection and Reconnaissance

## Slide 33: Detection and Reconnaissance
Aircraft are often used for detection and reconnaissance of fires:
Ability to cover vast areas in a short time to detect or find fires.
Better visual vantage point for reconnaissance.
Sometimes the only safe or possible way to monitor the fire’s behavior is by aircraft.

## Slide 34: Detection and reconnaissance
NOTE: Aircraft is not a substitute for a ground-based lookout on a fire.

## Slide 35: Detection and Reconnaissance
Single or small twin-engine airplanes used:
  For flights above 500 feet
  To cover long distances
  To monitor fire for long durations

## Slide 36: Helicopters Used
For special use missions (flights lower than 500 feet AGL)
For close scouting and mapping of the fire perimeter

## Slide 37: Infrared Mapping System

## Slide 38: Infrared Mapping SYSTEM
Heat detecting devices, which can be mounted or operated from an aircraft to allow firefighters to:
  Determine where the fire is burning during poor visibility conditions.
  Locate hot spots not easily detected outside the fire perimeter.
  Assist in mop up by pinpointing heat sources.

## Slide 39: Infrared Mapping

## Slide 40: Aerial Photography and Video Recording
Fire behavior documentation
Training purposes
Public relations (news media)

## Slide 41: Medical Aid
Airplanes and helicopters are used to deliver medically trained personnel.
Helicopters are often the only means of evacuating injured personnel.

## Slide 42: Search and Rescue (SAR)

## Slide 43: Selection of Aircraft for the Mission
First, you must determine if an aircraft
is absolutely necessary or can the
mission be accomplished by other
ground resources.

## Slide 44: Selection of Aircraft for the Mission
Specific aircraft for missions are
selected and assigned based on the
following criteria:
Aircraft operational requirements
Payload

## Slide 45: Selection of Aircraft for the Mission
Special Considerations:
Aircraft speed
Aircraft range
Aircraft cost
Mission accomplishment
Logistics
Landing site

## Slide 46: Air-to-Ground Communications

## Slide 47: Use of Radios
Air-to-ground frequency normally designated and known by ground personnel and pilots.
Air-to-ground frequency may be discrete frequency or assigned tactical frequency for your division or fire.
During IA, this may be the forest net.

## Slide 48: Radio Use
Be sure assigned frequencies are programmed in your radio:
Preassigned initial attack frequencies.
Incident assigned air-to-ground frequency.
Air guard frequency can be used for emergency or establish initial contact with aircraft (all aircraft must monitor this frequency).

## Slide 49: Target Description (TD)
TD is a systematic technique:
Meant to enable the pilot to locate and identify the target.
Accomplished by radio communication between the ground contact and the pilot.
Meant to communicate the target description and the target location.

## Slide 50
Purpose of TD:
To have the aircraft in the “low and slow” zone the shortest amount of time possible to reduce risk exposure to air and ground personnel.

## Slide 51: The Ground Contact Communicates with:
Air Tanker Pilot
Air Tanker Coordinator
(ATCO)
Lead Plane Pilot
Helicopter Pilot
Helicopter Pilot
Helicopter Coordinator
(HLCO)
Air Tactical Group Supervisor (ATGS)
or
Aerial Supervision Module (ASM1)

## Slide 52: Before Contacting Aircraft
Need to know:
Hazards to aircraft
Your location
Your call sign
Your tactical objectives (plan)
Aircraft call sign
Aircraft frequencies
Primary and secondary targets
Wind speed and direction

## Slide 53: Where do you get this information?
Helibase
IAP (ICS 204 and 220)
Appropriate incident supervisor
Personal observations
Radio traffic
Briefings

## Slide 54: Operating Procedures
Use the ICS aerial supervision resources to request and coordinate drops:
  ATGS
  HLCO
  ATCO

## Slide 55: Operating Procedures
Have and know the tactical plan:
  Anchor & flank
  Hot spot
  Buy time
  Secure the edge

## Slide 56: Operating Procedures Use standard fire terminology
Head
Spot Fire
Left Flank
Right Flank
Hot Spot
Heel

## Slide 57: Operating Procedures
Use standard target orientation techniques:
  Parts of the fire
  Clock orientation
  Right, left, nose, tail
  High, even, low
  Cardinal points (north, south, east, west). only use if you and pilot agree which way is north.

## Slide 58: Clock Orientation Exercise:
From the following slides, establish yourself as a reference point using the clock orientation technique and if you are high, even, or low.

## Slide 59
You are here
3 o’clock Low
Describe Your Position (clock orientation)

## Slide 60
11 o’clock Even
You are here
Describe Your Position (clock orientation)

## Slide 61
Describe Your Position (clock orientation)
You are here
1 o’clock Low

## Slide 62
You are here (helicopter is dropping in front of you)
Describe Your Position (clock orientation)
12 o’clock Low

## Slide 63
Describe Your Position (clock orientation)
You are here
5 o’clock Low

## Slide 64
Describe Your Position (clock orientation)
You are here
4 o’clock Low

## Slide 65
Describe Your Position (clock orientation)
You are here
4 o’clock Low

## Slide 66
Describe Your Position (clock orientation)
You are here
8 o’clock Low

## Slide 67: TD Operating Procedures
Use easily identifiable target references such as:
  Extend previous drop
  From your position
  To topographic or terrain features
  To human-made features
  Part of fire or fire activity
  To cardinal points (agree with pilot which way is north)

## Slide 68: Reference to loads already dropped
“Extend to/from your previous drop”

## Slide 69
Human-Made Features such as roads, structures, etc.
Terrain Features such as draws, ridges, etc.

## Slide 70: Reference to Cut Areas (human-made)
“The dozer line on the left flank”

## Slide 71: Part of fire
Drop on head of fire, anchoring from road

## Slide 72: Reference to Cardinal Points
“The spot fire north of the lake”

## Slide 73: Describe target when pilot can see target!
Use clear text
Be brief, clear, and to the point
Plan your transmission before you key the radio
Don’t “think out loud” on the radio

## Slide 74: Stages of Pilot Orientation
Long distance
Medium distance
Short distance

## Slide 75: Long Distance Stage
Geographical and topographical reference points must be large and obvious.
GPS coordinates are useful if air crew has time to enter information.
Relay lat/longs to helibase or ATGS when ordering aircraft.
Radio contact but no visual contact with aircraft

## Slide 76: Long Distance Stage
Keep positive communication with aircraft until visual contact is established (both the ground contact and pilot).
Radio contact but no visual contact with aircraft

## Slide 77: Medium Distance Stage
Reference points must be obvious.
If aircraft is in sight, use the clock orientation technique.
Signaling devices are effective (mirrors, strobes, flares).
May or may not have visual contact with aircraft

## Slide 78: Medium Distance Stage
Keep positive radio communication until visual contact is established (both the ground contact and pilot).
Relay aerial hazards to pilot.
If appropriate, relay tactical plan to pilot.
May or may not have visual contact with aircraft

## Slide 79: Short Distance Stage
Reference point must be unique to your target area.
Clock orientation technique is effective.
Signaling devices are effective (mirrors, strobes, flares, space blankets, flagging).
Have visual contact with aircraft

## Slide 80: Short Distance Stage
Describe target(s) and give tactical plan to pilot.
Reemphasize aerial hazards.
Have visual contact with aircraft
If the aircraft is getting close and the pilot doesn’t have the target location, communicate any known aerial hazards!!!

## Slide 81: Feedback
Give an honest, constructive, and timely evaluation of the drop.
Early, late, uphill, downhill, on target, etc.
If conditions allow, pilot will adjust drop(s) based on your feedback.

## Slide 82: Sterile Cockpit Procedures
Sterile cockpit procedures means that we must maintain radio silence except in emergencies.
As a passenger, you must always adhere to safe practices.
Regardless of the type of airspace you are going into, you must maintain sterile cockpit procedures during approach and departure phases of flight.
This applies to aerial fire suppressant delivery.

## Slide 83: Sterile Cockpit Procedures
Upon pilot request, within 5-mile radius of an airport or target-area, there should be no communications within the aircraft.
Unless you need to inform the pilot of other aircraft or hazards, do not distract them from their takeoff or approach within 5 mile radius.
Are used:

## Slide 84
Aerial Fire Suppression
Operations

## Slide 85: Air Tactical Group Supervisor (ATGS)
On incidents where there are numerous aircraft
assigned, an ATGS will also be assigned to
coordinate the aircraft flights over the incident
(tactical and logistical) for safety and efficiency.

## Slide 86: ATGS Safety Responsibilities
Determines what aircraft are operating within area of assignment.
Determines and recommends aircraft needs for the incident.
Ensures that a good flight following plan is in place for all aircraft.

## Slide 87: ATGS Safety Responsibilities
Determines that adequate and appropriate FM and VHF radio frequencies are used.
Identify aviation safety issues and mitigates any hazards.
Responsible for airspace and air traffic management for incident.

## Slide 88: ATGS Safety Responsibilities
Establishes and maintains communications with Air Operations Branch Director, air tanker and Helicopter Coordinators, Helibase, fixed-wing bases, and ground resources.
Receives and acts on reports of nonincident aircraft violating TFR.

## Slide 89: ATGS Safety Responsibilities
Makes tactical recommendations to appropriate operations section personnel.
Informs Air Operations Branch Director of tactical recommendations affecting the air operations portion of the IAP.

## Slide 90: air tanker/fixed-wing Coordinator (ATCO)
Establishes communication with the ATGS and obtains operational briefing on overall strategy and tactics.
Establishes communication with the air tanker pilot(s) and ensures compliance with the communication plan.
Surveys incident for hazards to ensure the safe operation of all aircraft.

## Slide 91: air tanker/fixed-wing Coordinator (ATCO)
Assigns air tanker(s) to specific tasks based on the action plan and the limitations of the air tanker(s).
Ensures that the air tanker pilot understands the overall strategy and tactics.
Coordinates with the ATGS for safe separation of rotor and fixed-wing aircraft.

## Slide 92: air tanker/fixed-wing Coordinator (ATCO)
Gives direct supervision to air tankers. Will lead air tankers on specific runs to ensure safe drops and exit route.
Can fulfill some responsibilities of the ATGS if requested.

## Slide 93: air tanker Pilot
Deliver retardant at the direction of the ATCO.
Confirm with the ATCO that the tactics and strategy are appropriate.
Communicate with the ATCO on air tanker capabilities and limitations.

## Slide 94: air tanker Pilot
Air tanker Captain, in conference with the co-pilot, has the final authority on the mission.
Air tanker pilots carded for initial attack can assume some of the responsibilities of the ATCO and the ATGS in their absence.

## Slide 95: Helicopter Coordinator
Establishes communication with the ATGS and obtains operational briefing on overall strategy and tactics.
Establishes communication with the incident helibase to determine logistical needs of incident to be supported by helicopter.

## Slide 96: Helicopter Coordinator
Surveys incident for hazards to ensure the safe operation of all aircraft.
Assigns helicopters to specific tasks based on incident action plan and the capabilities and limitations of the assigned helicopter(s).

## Slide 97: Temporary Flight Restriction (TFR)
To keep nonincident aircraft out of the
incident airspace for safety purposes, a
TFR may be requested by incident
aviation management.

## Slide 98: Temporary flight restriction (tfr)
Incident dispatch will make formal TFR request to Federal Aviation Administration (FAA).

## Slide 99
Think of a standard TFR as having the attributes of a cylinder placed over a piece of land (fire area)
Vertical
height
Radius
Center point

## Slide 100
A TFR shape can be:
Circular – Single incident
Noncircular – To accommodate multi-incidents
Temporary Flight Restriction (TFR)

## Slide 101: TFR
If TFR is approved, FAA will issue notification that all nonincident aircraft must avoid entering the TFR area.
When TFR is no longer needed, the incident dispatch will make a request to the FAA to cancel the TFR.

## Slide 102: Aerial Fire suppressant Delivery

## Slide 103: air tankers

## Slide 104
Air Tanker Base

## Slide 105
Some air tankers
can reload from large lakes and rivers.

## Slide 106: Single-Engine air tanker (SEAT)

## Slide 107: P2V Tank and Doors
Air tankers have various tank configurations.

## Slide 108: Coverage Level
Number of
gallons of
retardant
covering
100 ft2 of fuel on the ground

## Slide 109: Coverage Level
Coverage Level
#1 (1 gal/100 ft2)
#2 (2 gal/100 ft2)
#3 (3 gal/100 ft2)
#4 (4 gal/100 ft2)
#6 (6 gal/100 ft2)
#6+ (6+ gal/100 ft2)
FB Fuel Model
1, 2
2, 8, 9
3, 5, 11
10
4, 6
4, 12, 13

## Slide 110: Trail Drop

## Slide 111: Salvo Drop

## Slide 112: Retardant should fall as mist or light rain

## Slide 113: Minimum Drop Height
200 feet above canopy for Type 1-3 air tankers
60 feet above canopy for Type 4 (SEATs)

## Slide 114: Accuracy
Accuracy is a function of a number of
factors:
Density altitude
Ground speed
Drop height
Aiming error
Line of flight
Wind and mountain currents
Equipment (release) response time
Variability in drop trajectory

## Slide 115: Helicopters

## Slide 116: Bucket systems
Buckets range from 72 to 3,000 gallons.

## Slide 117: Collapsible Bucket

## Slide 118: Collapsible Bucket

## Slide 119: Rigid Bucket

## Slide 120: Semirigid Bucket

## Slide 121: Fixed Tank Systems

## Slide 122: Fixed Tank

## Slide 123: Fixed Tank and Snorkel

## Slide 124: Fixed Tank and Snorkel

## Slide 125: Portable Retardant Base

## Slide 126: 6 Minutes for Safety
Handout: Working With Helicopter Drops

## Slide 127: Exercise: Retardants and suppressants
Read the “Basic Guide for Use of Aerial Retardant” in student workbook, pages 3.43 to 3.50.
Answer four questions:
1. Define retardant.
2. Define suppressant.
3. List six factors to consider before using retardant.
4. List six indicators of effective retardant use.

## Slide 128: Exercise Answer
Define Retardant:
A fire suppression chemical mixture or formulation applied ahead of a fire front to reduce rate of spread or intensity.

## Slide 129: Exercise Answer
Define Suppressant:
A fire suppression chemical mixture or formulation, including water, applied directly to a fire, usually at the base of the flames to suppress the flames, not just to prevent their spread.

## Slide 130: Exercise Answers
Factors to consider before using retardant:
Values at risk
Availability of other fire suppression resources
Fire behavior
Purpose of retardant use
Availability of air tankers and retardant
Flight conditions

## Slide 131: Exercise Answers
Indicators of effective retardant use:
Retardant hit intended target.
Fire intensity or rate of spread is reduced or stopped.

## Slide 132: Exercise Answers
Indicators of effective retardant use:
Penetrated the forest or fuel canopy
Fell as light rain or mist

## Slide 133: Exercise Answers
Indicators of effective retardant use:
Ground forces are available to follow up.
Continuous drops can be made to support ground forces.
Allowed you to catch up or buy time you needed.

## Slide 134: Safety Procedures During Aerial Operations

## Slide 135: Low Drop Accident

## Slide 136
Retardant spray and shrapnel damage
Aircraft engine landed 6 feet from fire engine
Low Drop Accident

## Slide 137: Before air tanker Makes a Drop
ATGS will assure drop zone is clear.
If no ATGS, air tanker coordinator (lead plane) or air tanker will make a low level dry run over drop area.
Move out of drop area.

## Slide 138: Stay Clear of Helicopter Drops
Rotor wash
Dislodged branches and limbs
Blow over standing snags
Dropped and damaged bucket

## Slide 139: Before air tanker Makes a Drop
Clear area by moving away, at right angle to flight path, at least 200 feet.
Clear of snags. Move away 1-1/2 times the height of the tallest snag.
Watch for dislodged materials.
Wet retardant is slippery. Watch your footing when working in drop areas.

## Slide 140: If caught in retardant drop area
Lie face down
Hard hat (with chinstrap fastened) toward approaching plane
Hold tool on downhill side
Oncoming plane

## Slide 141: air tanker and Helicopter Tactics

## Slide 142: Indirect Attack
Ridgeline
Usually a large fire tactic.
A considerable distance away from fire edge.
Use natural barriers.
Burn out between.

## Slide 143: Pretreat Fireline

## Slide 144: Direct Attack
Working directly on the fire edge

## Slide 145: Direct Attack

## Slide 146: Parallel Attack
Move off fire edge a short distance.
Take advantage of light fuels or barriers.
Straighten ragged fire edge
Burn out between.

## Slide 147: Tying in the line for parallel attack

## Slide 148: Aerial Ignition Systems

## Slide 149: Helitorch
An aerial ignition device, suspended by cables below a helicopter, which ignites and dispenses a gelled gas mixture

## Slide 150: Helitorch

## Slide 151: Logistical Support for a Helitorch Operation
No passengers are allowed in the helicopter.
Only trained and qualified personnel shall assist with supporting helitorch operations.

## Slide 152: Premo MK III
Aerial Ignition Device
Plastic Sphere Dispenser

## Slide 153: Plastic Sphere Dispenser Mounted in Helicopter

## Slide 154: Must be trained and qualified to operate
Only operator and Ignition Specialist may be on board.

## Slide 155
BURNING SPHERE

## Slide 156: Circular burn patterns from spheres

## Slide 157: Special Operations

## Slide 158: Special Operations
Nonfire Missions
Within the Federal
government, agencies
depend on aircraft
to do their daily
operations.
Each natural resource project requiring the use of an aircraft may require a Project Aviation Safety Plan (PASP).

## Slide 159: Special Operations
Animal Capture and Eradication
(ACETA)

## Slide 160: Special Operations
Aerial Seeding
Aerial seeding may
require an aircraft to dispense the seeds over a large area.

## Slide 161: Special Operations
Law Enforcement
Patrol
Surveillance
Access to remote area
Drug interdiction

## Slide 162: Special Operations
Other Missions
Forest health
surveys
Military operations
Short haul
Hydro mulch
Cone collection
Habitat restoration

## Slide 163: Unit 3 Objectives
1. Define tactical and logistical use of aircraft.
Identify the advantages and disadvantages of the various tactical aircraft missions.
Identify the different logistical aircraft missions and their purpose.

## Slide 164: Unit 3 Objectives
4. Describe the proper air-to-ground communication procedures.
Describe safety procedures to follow during aerial fire suppression operations.
Describe Special Operations.