## Slide 1: Unit 3

## Slide 2: Unit 3 Objectives
Identify and describe basic wildland fuel characteristics.
Identify and describe seven characteristics of fuels that affect wildland fire behavior.
Identify and define by size class the four dead fuel timelag categories used to classify fuels.
Describe how fuel availability is essential to predicting wildland fire behavior.
Describe the fuel model concept and its utility for predicting wildland fire behavior.

## Slide 3: Fuel Make-up
Fuel characteristics
Fuel moisture
Fuel temperature

## Slide 4: Fuels
Any combustible material that:
  Is living or dead
  Is in or on the ground
  Is in the air
  Can ignite and burn
3-4-S290-EP

## Slide 5: Fuel Combinations
Kind
Amount
Size
Shape
Position
Arrangement

## Slide 6: Fuel Levels and Components
Ground
Surface
Aerial fuels

## Slide 7: Ground Fuels
All combustible materials lying beneath the surface:
    Deep duff
    Tree roots
    Rotten buried logs
    Other organic material

## Slide 8: Ground Fuels
Important in terms of line construction and mop-up
Typical fire spread:
  smoldering
  creeping

## Slide 9: Surface Fuels
All combustible materials lying on or immediately above the ground:
    Needles or leaves
    Duff
    Grass
    Small dead wood
    Downed logs
    Stumps
    Large limbs
    Shrubs to about six feet in height
    Litter

## Slide 10: Surface Fuels
Less compact than ground fuels
Have other characteristics more favorable for faster rates of spread
Fires often have higher rates of spread
Most wildfires ignite in and are carried by the surface fuels

## Slide 11: Surface Fuels
Important in terms of line construction and mop-up, most important regarding fire spread and fire behavior

## Slide 12: Aerial Fuels
All green and dead materials located in the upper canopy:
    Tree branches and crowns
    Snags
    Hanging moss
    Tall shrubs

## Slide 13: Aerial Fuels
Open canopy:
Faster spreading surface fire than closed canopy stands.
  Torching of individual trees
  Crowning is unlikely

## Slide 14: Aerial Fuels
Closed canopy:
Greater than 6 feet in height.
Best opportunity for a running crown fire.
Canopy closure is usually given in percent.
  25 percent of the ground is visible, there is 75 percent canopy closure.

## Slide 15: Aerial Fuels
Important in terms of fire spread and fire behavior due to torching, crowning, and spotting.

## Slide 16
Closed Canopy
Open Canopy
Please allow animation time to complete.
This slide demonstrates
the difference between
closed and open canopy

## Slide 17: Seven Characteristics of Fuels that Affect Wildland Fire Behavior
Seven principal characteristics:
    Fuel loading
    Size and shape
    Compactness
    Horizontal continuity
    Vertical arrangement
    Moisture content
    Chemical content
Two main categories:
    Physical and chemical characteristics
    Moisture content

## Slide 18: Fuel Loading
The amount of fuel present expressed quantitatively in terms of weight of fuel per unit area.
Measured in:
tons/acre (tons/acre)
OR
pounds/acre (lbs/acre)

## Slide 19: Loading Varies by Fuel Group
Grass
<1-5 Tons/Acre
Shrub
2-80 Tons/Acre
Slash
10-200 Tons/Acre
Timber Litter
4-12 Tons/Acre

## Slide 20: Size and Shape
Surface area to volume ratio

## Slide 21: Size and Shape
Small fuels ignite and sustain combustion easier than large pieces of fuel.
Click image to play video clip

## Slide 22: Size and Shape
Higher ratios burn more readily
Lower ratios do not burn as readily

## Slide 23: Size and Shape
Firebrands
Small embers
  Ordinarily produce short-range spotting
  Cannot sustain combustion
Flatness and greater surface-area-to-volume ratios have increased the aerodynamic qualities
Examples:
  Cedar fronds
  Bark plates
  Pine needles

## Slide 24: Size and Shape
Rolling firebrands
Important to spotting downslope
Examples:
  Pine cones
  Round logs
  Round yucca plants

## Slide 25: Compactness = Spacing Between Fuel Particles
Closely compacted
  Less surface area exposed
  Restrict oxygen
  Inhibit convective and radiant heat transfer
  In most cases, slower rate of spread is expected
Loosely compacted
  Normally react faster to moisture changes
  Have more oxygen available for combustion
  Rate of spread is usually greater

## Slide 26: Fuel Bed Depth and Orientation
Fuel Bed
  The average height of surface fuel that is contained in the combustion zone of a spreading fire front.
Orientation
  The horizontal or vertical orientation of the fuel array that carries the fire.

## Slide 27: Vertically Oriented Fuels
Fuel load increase
Fuel bed depth increases rapidly
Average depth of fuels
1.5
1
.5
4
3
2
1
FEET
TONS/AC
Grass group
Shrub group

## Slide 28: Horizontally Oriented Fuels
Fuel load increase
Fuel bed depth increases slowly
Average depth of fuels
Timber litter group
Slash group
3
2
FEET
TONS/AC
2
1
1.50
2
2
1.25
Average depth of fuels
Slash
Litter

## Slide 29: Horizontal Continuity
Horizontal distribution of fuels at various levels or planes.
Characteristics influence:
  Where a fire will spread
  How fast fire will spread
  Whether fire travels through
    Surface fuels
    Aerial fuels
    Both

## Slide 30: Continuous vs. Patchy Fuels
3-30-S290-EP

## Slide 31: Aerial Fuels
Closed Open
20 mph
2 mph
5 mph
3-31-S290-EP

## Slide 32: Vertical Arrangement
Fuels above ground and their vertical continuity, which influences fire reaching various levels or vegetation strata.
3-32-S290-EP

## Slide 33: Ladder Fuels

## Slide 34: Reburn
3-34-S290-EP

## Slide 35
Precipitation
Dew
Ground moisture
Fuel Moisture Content
Humidity
Evaporation
Evaporation
3-35-S290-EP

## Slide 36: Live and Dead Fuel Moisture
Dead Fuel Moistures – rarely below 3-4%, fluctuate often due to environmental conditions.
Live Fuel Moistures – range much higher, with moisture contents of perhaps as high as 300% or more, fluctuate much more slowly, relate to growing season.

## Slide 37: Fine Dead Fuels
Are considered the primary carrier of a surface fire.
Consist of needle/leaf litter, cured out grass.

## Slide 38: Live to Dead Ratio

## Slide 39: Chemical Contents
All fuels, living or dead, contain fiber that is known as cellulose.
Include, but are not limited to certain volatile substances such as:
    oils
    resins
    wax
    pitch

## Slide 40: Chemical Contents
Volatile fuels:
    Chaparral in the southwest
    Palmetto in the southeast
    Greasewood in the Pacific northwest
    Fountaingrass in Hawaii
    Pitchy stumps from some conifers
    Jack Pine in the Lake States
    Pitch Pine in the northeast

## Slide 41: Fuel Characteristics/Fire Behavior
Compactness
Loading
Horizontal
Continuity
Vertical
Arrangement
Chemical
Content
Moisture
Content
Size and
Shape
3-41-S290-EP

## Slide 42: Fuel Characteristics
Five fuel characteristics that most effect ignition:
    Compactness
    Loading
    Chemical content
    Size and shape
    Moisture content

## Slide 43: Fuel Characteristics
Ignition
Spread
Intensity
Spotting
Torching
Crowning
Six primary fire behavior characteristics involved with the rate of spread:

## Slide 44
Timelag
Time needed under specified conditions for a fuel particle to lose about 63 percent of the difference between its initial moisture content and its equilibrium moisture content.

## Slide 45: Dead Fuel Timelag Categories
1-hour
10-hour
100-hour
1000-hour
Which category gains/loses moisture the fastest?

## Slide 46
Available Fuels
Grass
Up to 100%
Shrub
5-95%
Slash
10-70%
Timber litter
5-25%
Fuels that will ignite and support combustion at the flaming front under specific conditions.

## Slide 47: Consumption of Various Fuels by Fires
The following play an important part in a fuel's availability to burn:
    Size
    Arrangement
    Moisture content
    Duration and intensity of the fire

## Slide 48: Fuel Characteristics and the Fuel Model
FUEL MODEL
Vertical
arrangement
Moisture
content
Size and
Shape
Loading
Chemical
content
Compactness
Horizontal
continuity

## Slide 49: Fuel Models
13 models:
Grass (3 fuel models)
Shrub (4 fuel models)
Timber Litter (3 fuel models)
Slash (3 fuel models)

## Slide 50: Fuel Models
Anderson’s Aids to Determining Fuel Models for Estimating Fire Behavior

## Slide 51: Major Fuel Groups
The four major fuel groups are:
    Grass
    Shrub
    Timber Litter
    Slash

## Slide 52: Grass Group
Grass is primary carrier of fire
Fuel bed: 1’ to 2.5’ deep
Fuel Characteristics:
  300 lbs/acre to several tons/acre
  Usually < 0.25” in diameter
  Compactness
  Moisture content changes rapidly due to changes in RH
Fire Behavior: rapid burnout, low intensity,
wind strong influence,
ROS 35 to 100+ ch/hr,
FL 0 to 12 ft

## Slide 53: Shrub Group
Shrub is primary carrier of fire
Fuel bed: 2’ to 6’ deep
Fuel Characteristics:
  1 to 80 tons/acre
  Usually < 1” in diameter, dead + live fuels
  Compactness: loosely layered to very deep
  Some volatiles may be present
Fire Behavior: very low to extreme intensities,
wind strong influence,
ROS 18 to 75 ch/hr,
FL 4 to 19 ft

## Slide 54: Timber Litter Group
Surface litter is primary carrier of fire
Fuel bed: 0.2’ to 1’ deep
Fuel Characteristics:
  Size and shape mixed: litter, leaves, needles to large branchwood
  Compactness: loosely layered to compact
  Vertical arrangement < 1’, typically < 3”
  Moisture content retained when litter is compact
Fire Behavior: slow burning to running surface
fires, torching, crowing possible,
ROS 2 to 8 ch/hr, FL 1 to 5 ft.

## Slide 55: Slash Group
Slash is primary carrier of fire
Fuel bed: 1’ to 3’ deep
Fuel Characteristics:
  Size and shape all sizes
  Fuel loading between 12 and 58 tons/acre
Fire Behavior: moderate to rapid spread rates, moderate to high intensities dependent on fuel arrangement, ROS 6 to 14 ch/hr, FL 4 to 11 ft, firebrands often produced and lifted into convection column, rolling materials may start spot fires

## Slide 56: Group vs. Model
Grass Group:
Fuel Model 1 Short Grass (<1 foot high)
Fuel Model 2 Timber (grass and understory) Fuel Model 3 Tall Grass (2 feet high)
Shrub Group:
Fuel Model 4 Chaparral (6 feet)
Fuel Model 5 Short Brush (2 feet)
Fuel Model 6 Intermediate Brush
Fuel Model 7 Southern Rough

## Slide 57
Timber Litter Group:
Fuel Model 8 Closed Timber Litter
Fuel Model 9 Hardwood Litter
Fuel Model 10 Timber (litter and understory)
Slash Group:
Fuel Model 11 Light slash
Fuel Model 12 Moderate slash
Fuel Model 13 Heavy slash
Group vs. Model

## Slide 58: Introduction to the Standard Fire Behavior Fuel Models
The new Standard Fire Behavior Fuel Models, sometimes referred to as “the 40 fuel models.”

## Slide 59: New Model Parameters
Load by class and component
Surface-area-to-volume (SAV) ratio by class and component
Fuel model type (static or dynamic)
Fuelbed depth
Extinction moisture content
Fuel particle heat content

## Slide 60: Need for the New Models
Original 13:
For the severe period of the fire season.
Have worked well for predicting spread rate and intensity at peak of fire season.
Have limitations for other purposes:
  Prescribed fire
  Wildland fire use
  Simulating the effects of fuel treatments on potential fire behavior
  Simulating transition to crown fire using crown fire initiation

## Slide 61: Need for the New Models
New Models:
Improve the accuracy of fire behavior predictions outside of the severe period of the fire season.
Increase the number of fuel models:
  Applicable in high-humidity areas.
  For forest litter
  For litter with grass
  For shrub understory
Increase the ability to simulate changes in fire behavior

## Slide 62
Grass
New Fuel Groups
Grass - Shrub

## Slide 63
New Fuel Groups
Shrub
Timber - Understory

## Slide 64
New Fuel Groups
Slash - Blowdown
Timber - Litter

## Slide 65: Unit 3 Objectives
Identify and describe basic wildland fuel characteristics.
Identify and describe seven characteristics of fuels that affect wildland fire behavior.
Identify and define by size class the four dead fuel timelag categories used to classify fuels.
Describe how fuel availability is essential to predicting wildland fire behavior.
Describe the fuel model concept and its utility for predicting wildland fire behavior.